# BRAKE FLUID DOT 4

Special brake fluid for braking discs system

Applications:

•GEDOL BRAKE FLUID DOT 4 is recommended for brake and clutch systems of all vehicles using synthetic fluids when a DOT 4 level is required.

• GEDOL BRAKE FLUID DOT 4 is miscible with all other synthetic fluids of similar quality.

• GEDOL BRAKE FLUID DOT 4 is not miscible with mineral based fluids (LHM) and silicon based fluids.

•The color of the product can vary from colorless to amber.

Customer benefits:

- Synthetic fluid.

- Very high dry and wet boiling points adjusted to ever increasing temperatures encountered in braking systems : prevents from "vapour lock".

- Resistant to moisture absorption.

- Viscosity suitable at cold as well as high temperatures.

- Provides corrosion protection for metals used in braking systems : cast iron, aluminium, steel, copper, brass etc.

- Compatible with rubber seals and hoses.

PERFORMANCES LEVELS                                                      SPECIFICATIONS*

|  |  | DOT 4 |
| --- | --- | --- |
| FMVSS 571 116 DOT4, |  |  |
| SAE J 1703 D, J 1704 | Specific gravity at 20°C | 1,05 |
| ISO 4925 | Viscosity cSt at –40°C | 1.600 max |
| CUNA NC 956-01 | Viscosity cSt at 100°C | 2,3 |
|  | Dry boiling point °C | 260 |
|  | Wet boiling point °C | 160 |

*The values given in this specifications table are typical values for information purposes only