#### LE MANS SYNTH 10W/40

Very high performance lubricant semi-synthetics technology, specially developed for Gasoline and Diesel car engines, answering the enhanced requirements of the latest direct injection technologies

Applications

- All Gasoline and Diesel engines

- Direct and indirect Injection

- All times of year

- Recommended for all Gasoline and Diesel engines in cars and light vans.

- Specially adapted to the requirements of modern technology Diesel engines, namely the direct injection with or without Common Rail.

- Fully adapted to all types of service (in town, on highways and motorways),

Refer to the maintenance book of your vehicle to know the recommendation of the manufacturer.

Customer benefits:

- Very high performance

- Enhanced Properties specific to Diesel engines

- Lengthens engine life

- GEDOL LEMANS SYNTH 10W40 semi-synthetic technology, ensuring sustainable performance over the time, thus meeting the needs of the OEMs in terms of extended oil drain intervals.

- Excellent detergent properties giving greater engine cleanliness for better performance.

- Specially designed to meet the particular requirement of direct injection engines. Direct injection improves power and low-speed torque, and reduces fuel consumption, but also increases the operating temperature. It is therefore important to use a lubricant able to protect the engine at high temperature.

- Wide viscosity index range giving the lubricant excellent performance at high temperature, and ensuring rapid lubrication of engine components during cold starts. This optimal protection at any temperature extends engine life.

###### PERFORMANCES LEVELS                                           SPECIFICATIONS*

| API SM/CF | Viscosity Grade SAE 10W/40 |
| --- | --- |
| ACEA A3-B3/B4 | Specific gravity at 15 °C 0,876 |
| Mercedes Benz MB 229.1 | Viscosity cSt at 100°C 14 |
| VOLKSWAGEN 500.00 - 502.00 | Viscosity CCS at –25°C, Cp <7000 |
|  | Viscosity Index 155 |
|  | Flash Point C.O.C °C 226 |
|  | Pour Point °C - 33 |

*The values given in this specifications table are typical values for information purposes only.