WINNER SPECIAL 5W/30

The new generation of Low SAPS engine oil specially formulated to meet the technical requirements of Volkswagen group vehicles. Its very high-tech performance optimises the way in which anti-pollution systems - such as Particulate Filters - operate

Applications:

• GEDOL WINNER SPECIAL 5W/30 is suitable for all Gasoline and Diesel engines, including the most recent, which comply with Euro V polluting emissions reduction norms in particular.

•It optimises anti-pollution systems, Particulate Filters (PF) in particular.

•It provides engines with excellent protection against wear, ensures they stay ultra clean and allows for longer intervals between oil changes.

•It performs even in the most demanding driving conditions (city, major roads, motorways). It is suited to every kind of driving style, especially sporty, high-speed and all-season driving.

Customer benefits:

•Increased life of particulate filters - Ensure the Particulate Filter lifetime, preventing it from getting clogged up prematurely (its metallic component content is lower than that of an oil made using conventional technology).

•Respect for the environment - Environmentally friendly, ensures that the engine's anti-pollution systems perform optimally.

•Engine protection and cleanliness - Provides the engine with excellent protection and ensures that it remains clean

•Longer intervals between oil changes - Exceeds standards in ensuring engine sustainability and satisfies the most demanding manufacturer service plans by allowing for extra-long oil change intervals, thanks to excellent resistance levels against oxidation

PERFORMANCES LEVELS                                        SPECIFICATIONS*

| ACEA -A1/B1 -A5/B5 C3 | Viscosity Grade SAE 5W/30 |
| --- | --- |
| VOLKSWAGEN 504.00-507.00 | Specific gravity at 15°C 0,868 |
| MB 229.31-229.51 | Viscosity cSt at 100°C 11,1 |
| BMW LL04 | Viscosity CCS at -30°C, a cP <6600 |
| API SN/CF | Viscosity Index 170 |
|  | Flash Point C.O.C. °C 225 |
|  | Pour Point °C -38 |

*The values given in this specifications table are typical values for information purposes only